## Slide 1
Transmission Planning in ERCOT- Overview
Nemica Kadel
System Planning Engineer
September 12, 2017

## Slide 2: Talk Outline
ERCOT Quick Facts
Regional Transmission Planning
Long Term System Assessment
Project Identification and Justification

## Slide 3: ERCOT Quick Facts
75% of Texas land
90% of Texas load – 24 million consumers
More than 46,500 miles of transmission lines
570+ generation units
Notes: Source: ERCOT Quick Facts: http://www.ercot.com/about/profile

## Slide 4: ERCOT Quick Facts
>77,000 MW peak capacity
71,110 MW record peak demand (set August 11, 2016)
Physical assets owned by transmission providers and generators
No synchronous connections with other grids
Notes: Source: ERCOT Quick Facts: http://www.ercot.com/about/profile

## Slide 5: ERCOT Quick Facts
DC East at Monticello (with SPP) – 600 MW
DC North (with SPP), at Oklaunion – 220 MW
DC Laredo; VFT (with CFE) – 100 MW
SPP: Southwest Power Pool
CFE: Comisión Federal de Electricidad
DC Ties: Direct Current ties – Asynchronous connections with neighboring grids
VFT: Variable Frequency Transformer
DC South at Eagle Pass (with CFE) – 36 MW
1,256 MW power transfers from non-synchronous ties
DC Railroad at McAllen; Sharyland Utilities (with CFE) – 300 MW

## Slide 6: ERCOT Quick Facts
Notes: Source: ERCOT Quick Facts: http://www.ercot.com/about/profile

## Slide 7: Reliability
ERCOT’s primary responsibility is to ensure the reliability of the grid.
  Match generation with system demand.
  Ensure the transmission system is operated within established limits.

## Slide 8: Reliability: Energy and Capacity
System Demand
Generation Output
Capacity
Forecast
ERCOT dispatches energy to meet system demand.
ERCOT must also ensure there is enough capacity on-line to meet forecasted demand.

## Slide 9: Reliability: Capacity Reserves
ERCOT must also ensure the system can respond to sudden changes in demand.
This is accomplished through additional capacity beyond the forecasted load
Called Ancillary Services
Forecast
System Demand
Reserved
Ancillary Service
Capacities
System Capacity

## Slide 10: Reliability: Transmission Congestion
Generation and loads separated by physical distances connected by transmission lines
Lines have ratings that cannot be exceeded
ERCOT is responsible for adjusting generation levels to mitigate congestion on the transmission system

## Slide 11: Transmission Planning at ERCOT
Transmission Planning Assessment
  Regional Transmission Plan (RTP)
  Long Term System Assessment (LTSA)
Dynamics Studies Group
  Ad-hoc System Stability Assessments
  Annual NERC stability assessments
  Subsynchronous Resonance Studies (SSR)
  Support Operations on stability issues
System Development Group
  RPG Independent Reviews and Special Studies
  Quarterly Stability Assessment Screening Studies
  Screening Studies

## Slide 12: Regional Transmission Planning
Identify transmission projects to meet ERCOT System needs per ERCOT Planning Guide and NERC TPL-001-4 reliability standards.
Annual Assessment for near-term needs for six years planning horizon.
Coordinated planning process performed by ERCOT with extensive review and input by NERC registered Transmission Planners (TPs), Transmission Owners (Tos) and stakeholders.

## Slide 13: Regional Transmission Planning Study Method
Case Conditioning
Future transmission and generation review and update
Transmission Outages, Dispatch of variable generators and limit monitoring settings
Basecase Reliability Analysis
N-1 SCOPF
Additional Reliability Analysis
Multiple element outage analysis and extreme event analysis
Sensitivity analysis for at least 2 summer peak cases and 1 off-peak case
Load review and adjustment
Generator and Transformer outage analysis
Add or improve transmission projects to mitigate overloads
Long-lead time equipment analysis
Short circuit analysis
Economic Analysis
Perform economic analysis
Add or improve transmission projects that meet the economic criteria
Contingency Analysis for certain EHV contingencies

## Slide 14: Long Term System Assessment
Biennial evaluation of the potential needs of ERCOT’s extra-high voltage (345-kV) system in the 10 to 15 year planning horizon.
Identify long-term transmission needs by analyzing the reliability and efficiency of the ERCOT system under various scenarios.

## Slide 15: Long Term System Assessment Study Method
LTSA

## Slide 16: Challenges in Transmission Planning
Load Forecast
Generation Resource Mix
New and Emerging Technologies
Economic and Financial Constraints
R-O-W Limitations
Regulatory Uncertainty
Various Uncertainties and Risks

## Slide 17: ERCOT on Social Media
iPhone and Android apps
  Provide alerts through push notifications
  Load curve, conservation tips, wholesale prices, general info
  More than 10,000 downloads
Social Media
  Focus on timely information with frequent updates
  Twitter: Over 4,000 followers
  Facebook: Over 1,200 followers

## Slide 18
Questions?